## Slide 1: Smart Railway Level-Crossing Safety Controller with Emergency Override
Arduino Uno • Tinkercad simulation • scale-model prototype
Presented by Team 1:
V Chinmaya Datta
N Jathin
Ch Sai Krishna
S Konda Reddy
Notes: Introduce the project: a fail-safe level-crossing controller on an Arduino Uno, simulated in Tinkercad using only parts that work the same in real life.

## Slide 2: What the project is and why
The problem
Basic crossing logic (entry sensor on, exit sensor off) breaks for long or paused trains, and a failed sensor looks exactly like 'no train'.
The solution
An Arduino-based controller that counts axles in and out, estimates train speed to time the warning, and goes to a safe state when anything is doubtful.
What it controls
Road signals (green, yellow, red), a servo barrier, flashing railway LEDs and a buzzer, plus an emergency override button.
Student prototype for a scale model, validated in simulation. It is not a certified railway safety system.
Notes: A basic crossing only checks entry and exit flags. This one counts axles, predicts arrival and fails safe. Stress that it is a student prototype.

## Slide 3: Components used
Arduino Uno
The controller. Runs a non-blocking state machine.
2 force sensors
Entry and exit axle detection (model track).
Servo motor
The barrier arm, moved smoothly 1° at a time.
6 road LEDs
Green, yellow, red on two approaches, sharing 3 pins.
2 railway LEDs
Red warning flashers that alternate.
Piezo buzzer
Different patterns for warning, emergency, fault, stall.
Pushbutton
Emergency override on a hardware interrupt (D2).
Resistors, capacitor
10k, 470k, 470 Ω, 330 Ω, 220 Ω; 470 µF across servo power.
Notes: Every part simulated in Tinkercad is the same part you would use on a real breadboard.

## Slide 4: Circuit built in Tinkercad
Pin | Connected to
A0 | Entry force sensor
A1 | Exit force sensor
D2 | Emergency button
D3 / D4 / D5 | Road green / yellow / red (2 LEDs each)
D6 / D7 | Railway warning LEDs
D8 | Buzzer via 220 Ω
D9 | Servo (barrier)
Key details
Each sensor: FSR in parallel with 470 kΩ, 10 kΩ pull-down to GND. Road LEDs 470 Ω each, railway LEDs 330 Ω, 470 µF capacitor across the servo supply.
Notes: Walk through the diagram briefly: sensors on A0 and A1, road LEDs on D3 to D5, flashers on D6 and D7, buzzer on D8 through 220 ohms, servo on D9, button on D2.

## Slide 5: Sensing: axle counting
≈ 21
Idle reading (0.10 V)
300–900
Pressed (axle)
0
Broken wire = FAULT
Reading a press
Counts as pressed above 300 and released below 150 (hysteresis). Edges closer than 40 ms are ignored (debounce). One press equals one axle, so holding a press never double counts.
Counting axles
Entry sensor adds 1, exit sensor subtracts 1. The crossing reopens only when axles out ≥ axles in. This handles any train length and a train that pauses inside the section.
Notes: The 470k bypass is what makes failures visible: idle reads a small non-zero value, a broken wire reads zero. Entry adds, exit subtracts, reopen only when balanced.

## Slide 6: Inside one sensor: failures become visible
5 V
FSR
470 kΩ
to A0
10 kΩ
GND
In real life the 470 kΩ is soldered at the sensor end, so a cut in either lead reads 0.
Idle: reads about 21
Nothing pressed: 5 V × 10k ÷ (470k + 10k) ≈ 0.1 V.
Pressed: reads 300 to 900
FSR resistance drops, so the voltage rises. Above 300 counts as an axle.
Wire cut: reads 0
The 10 kΩ pulls the node to 0 V. A reading of 0 means FAULT, not 'no train'.
Notes: The 470k resistor keeps the idle reading above zero, so a broken wire (reading 0) can be told apart from an idle sensor.

## Slide 7: Speed and constant warning time
How it is calculated
speed = axle spacing ÷ gap between axles
ETA = distance to crossing × gap ÷ spacing
warning starts at first axle + (ETA − 5 s)
Defaults: 60 mm spacing, 600 mm to crossing.
Axle gap | Speed | ETA | Warning starts
1000 ms | 60 mm/s | 10 s | 5 s after first axle
500 ms | 120 mm/s | 5 s | Immediately
300 ms | 200 mm/s | 3 s | Immediately
Fail-safe
No second axle within 1.5 s: warn anyway.
Result
Normal sequence: 2 s yellow plus 1.35 s of barrier travel, so the barrier is down about 1.65 s before a train that holds its speed arrives. Slow trains are held off; fast trains get a warning at once, with a shorter yellow and a faster barrier. ETA assumes constant speed.
Notes: Speed comes from the first two entry axles because their spacing is known. Entry-to-exit speed is only known after the train has passed, so it is only logged.

## Slide 8: State machine (non-blocking)
1 CLEAR
Road green, barrier open
2 APPROACH
Speed → ETA, hold-off
3 WARNING
Yellow 2 s + beep
4 CLOSING
Red, barrier lowers
5 OCCUPIED
Counting axles in/out
6 EXITING
Out ≥ in, 1.5 s quiet
7 CLEARING
Barrier lifts, road red
Back to 1 CLEAR
Road green again
FAULT / EMERGENCY (from any state)
Road goes red (via yellow if needed), barrier closes and stays closed, flashers run and the buzzer sounds. FAULT is a long low tone; EMERGENCY is a fast beep. An operator must press the button to reset.
Notes: Seven normal states plus FAULT and EMERGENCY reachable from anywhere. The road never jumps from green to red; it passes through yellow, even in an emergency.

## Slide 9: One train, start to finish
0 s
First entry axle detected
1 s
Second axle: speed and ETA calculated
5 s
Warning: yellow, flashers, beep
7 s
Red; barrier starts lowering
≈ 8.4 s
Barrier closed, ~1.6 s before arrival
10 s
Train reaches the crossing
Exit
Exit axles counted until out ≥ in
+ 1.5 s
Quiet period over: barrier lifts, road red
Done
Barrier up: road green, train log printed
Times are measured from the first axle. Example: 60 mm axle spacing, 600 mm to the crossing.
Notes: Example for a slow train with a 1 s gap between the first two axles. A fast train skips the wait and starts warning at once.

## Slide 10: Emergency override and fault handling
Trigger | How it is detected | Response
Emergency button | Interrupt on D2, 300 ms debounce | Yellow 2 s, then red, barrier closed, fast beep. Second press reopens.
Wire break | Reading below 3 for 300 ms | FAULT (latched)
Stuck sensor | Pressed for more than 30 s | FAULT (latched)
Wrong order | Exit axle with nothing inside | FAULT (latched)
Stalled train | Occupied for more than 30 s | Siren alarm, barrier stays closed
A FAULT clears only when the operator presses the button and both sensors read healthy.
Notes: The button uses a hardware interrupt so it is never missed. The second press means the operator confirms the crossing is clear, because the controller cannot know that itself.

## Slide 11: Where the novelty comes from
Axle counting
Replaces simple entry/exit flags, as real railways do.
Constant warning time
Speed-based timing, no extra hardware needed.
Wiring-level fault detection
One 470 kΩ resistor per sensor makes failures visible.
Interrupt-driven override
No delay() anywhere, so a press is never missed.
Safe signal sequencing
Yellow before red, road stays red until barrier is up.
Same parts as real life
Nothing is simulator-only; Serial log gives per-train data.
Notes: Be honest: each idea exists in real railways. The novelty is combining them on a low-cost model with a fail-safe design, using only real parts.

## Slide 12: How it is tested
Test | Action | Expected result
Normal train | Entry twice about 1 s apart, then exit twice | Hold-off, yellow, red, barrier closes, then reopens; train log printed
Fast train | Entry twice about 0.3 s apart | Warning starts immediately
Single axle | Entry once and wait | Warning after 1.5 s (fail-safe)
Long train | Entry 4 times, exit 3 times | Stays OCCUPIED until the 4th exit
Emergency | Press button in any state | Yellow, red, barrier closed; second press reopens
Wrong order | Exit sensor first | FAULT; button acknowledges
Wire break | Disconnect the A0 wire | FAULT after about 0.3 s
In Tinkercad a 'press' means dragging the sensor slider up, then back to 0.
Notes: Demonstrate in this order. Remember to release the sensor fully between presses.

## Slide 13: Key takeaways
Safer logic
Axle counting replaces fragile entry/exit flags.
Smarter timing
Speed-based warning keeps the road blocked for less time.
Fails safe
Faults, stalls and emergencies all end in a red road and a closed barrier.
Built to be real
Every simulated part works the same on a real breadboard.
Thank you
Notes: Close on the four points, then invite questions.